## Slide 1: Research Update 3

## Slide 2: How to Determine # Dry Days in Excel
added new column is it zero
=IF([@[Daily Discharge (Mean)]]=0,1,0)
insert pivot table, year as row,
value as is it zero (dont need to count)
removed 1963 and 2020

## Slide 3: https://waterdata.usgs.gov/nwis/nwismap/?site_no=08401900&agency_cd=USGS https://snoflo.org/report/flow/new-mexico/rocky-arroyo-at-hwy-brd-nr-carlsbad/
Rocky Arroyo Gauging Station
-NW of Carlsbad,
-drainage Area: 285 sq. Mi
-not dammed

## Slide 4: Rocky Arroyo Flow Regime
no flow days exploration
  Turns out it only flows like 4 days a year…. So not much to explore in terms of dry days increasing
  Better to explore days with flow over time
  Flow is decreasing (both mean and # wet days)
Chart: Dry Days
| 1964 | 1965 | 1966 | 1967 | 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
 | 364 | 361 | 343 | 345 | 359 | 358 | 359 | 364 | 362 | 365 | 281 | 365 | 366 | 359 | 349 | 355 | 361 | 362 | 361 | 363 | 361 | 364 | 343 | 361 | 359 | 365 | 363 | 358 | 347 | 365 | 361 | 361 | 352 | 364 | 365 | 363 | 354 | 365 | 352 | 365 | 347 | 365 | 361 | 359 | 365 | 365 | 361 | 365 | 366 | 360 | 357 | 364 | 362 | 364 | 363 | 359
Chart: Wet Days
| 1964 | 1965 | 1966 | 1967 | 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
 | 2 | 4 | 22 | 20 | 7 | 7 | 6 | 1 | 4 | 0 | 84 | 0 | 0 | 6 | 16 | 10 | 5 | 3 | 4 | 2 | 5 | 1 | 22 | 4 | 7 | 0 | 2 | 7 | 19 | 0 | 4 | 4 | 14 | 1 | 0 | 2 | 12 | 0 | 13 | 0 | 19 | 0 | 4 | 6 | 1 | 0 | 4 | 0 | 0 | 5 | 8 | 1 | 4 | 1 | 2 | 6

## Slide 5: COOP Carlsbad Caverns Station 291480 https://wrcc.dri.edu/cgi-bin/cliMAIN.pl?nmccav
2/1/1930 – 7/17/2020
max/min/avg temp and precip at daily resolution
To access data: http://climate.ncsu.edu/cronos/?station=291480
DRI website doesn’t provide actual data, only gives climate normal based on data
Downloaded, title raw carslabd caverns stn climate data

## Slide 6: Carlsbad Caverns Station Results
removed years w/ <350 days of data
  Can specifically look into years
  normally wet or dry months missing?
  Judge accordingly to include or not
Month | Percent Contribution
Sep | 20.0%
Aug | 15.6%
Jul | 14.6%
Jun | 10.3%
May | 9.7%
Oct | 9.1%
Apr | 4.2%
Dec | 3.6%
Nov | 3.6%
Mar | 3.1%
Feb | 3.1%
Jan | 2.9%

## Slide 7: COOP Queen RANGER STATIOn 297176 https://wrcc.dri.edu/cgi-bin/cliMAIN.pl?nm7176
1/1/1963 – 3/31/1975 (contains 4044/4473 days)
daily precipitation (no temp)
To access daily data: http://climate.ncsu.edu/cronos/?station=297176
To access climate summaries: https://wrcc.dri.edu/cgi-bin/cliMAIN.pl?nm7176
***wrcc.dri.edu… does not provide actual daily data, they only compute averages and 30-year climate summaries, hence why 1981-2010 tab is completely null, no data (same for other stations)

## Slide 8: Queen Ranger Station Results
Year | Total Precip (in) | Count | Months Missing
1963 | 9.05 | 304 | Oct, Nov
1964 | 7.4 | 307 | Apr, Jun
1965 | 15.05 | 334 | Mar
1966 | 19.6 | 365 | 
1967 | 13.43 | 304 | Nov, Dec
1968 | 13.36 | 242 | Jan, Apr, May, Aug
1969 | 18.33 | 364 | 
1970 | 19.28 | 364 | 
1971 | 10.91 | 361 | 
1972 | 19.18 | 366 | 
1973 | 14.63 | 242 | Jan, Apr, Aug, Oct
1974 | 26.8 | 360 | 

## Slide 9: COOP Queen Station 297172 (no DRI climate summaries Exist For this station)
4/28/2000 – 3/7/2007
***2006 and 2007 are empty
Additional Queen station covering later period, .8 miles from Queen RS
max/min/avg temp and precip at daily resolution
Can download in standard or metric
To access data: http://climate.ncsu.edu/cronos/?station=297172
DRI website doesn’t provide actual data, only gives climate normal based on data
Downloaded, title raw carslabd caverns stn climate data

## Slide 10: Queen Station Results not valid, insufficient data
Year | Total Precip (in) | Count | Months Missing
2000 | 16.83 | 221 | April, 1/2 may
2001 | 12.8 | 349 | couple days in sep
2002 | 11.56 | 330 | Sep
2003 | 7.69 | 354 | < half sep and nov
2004 | 34.02 | 329 | 
2005 | 5.16 | 238 | july, aug, sep, oct

## Slide 11
Southern options: make sure they arent at too high elevation or on top of peak
The bowl, carlsbad (city), carslbad cav, pine springs, pinery
  Look into hourly to build individual storm hydrographs
    Focus in on single storm events to see what they look like, doesn’t matter if whole dat set isnt complete just need enough for single storm events
  Sam will look into better data for queen or carlsbad
  Used this climate data to show that.....
    Flash flooods do x
    There are x dry days in the mountain range per year
    Storms are getting flashier
    Dry days increasing etc
    Thinking about how that data can be manipulated to come up with a cnclusion \
    \
    How are they changing spatially or temporally
    If not changing, what do they look like?
    Build storm distribution for each of the stations,
      Define importants storm characteristics
      Ie amount, duration, etc
      Do for hourly and daily stations , duration total water, max min etc
      Send along to sam with raw data
      Possibly do with thesis could get sams help
      Goal:: have in the next month
      Daily data: mean median max min, is there a temporal trend?
      Stationarity paper from SWH!
      SUM: ddata from carlsbad caverns, hourly from from texas stations, hourly from carlsbad
        If data is unchanging, build a distribution
          Min, mean max dfor daily etc
          Duration, amount water, max amount, etc for hourly (more specific, singular storm events / characteristics to help rebuild storm in landlab)
          -use daily station to justify wether water cycle is changing or unchanging in a certain area
          -hourly data used to reconstruct storms (if determined it is unchanging)
          Avg min max dev for average hillslopes in 5 channels